## Slide 1
INDUSTRIAL ADDITIVE MANUFACTURING
Converting a KUKA Robot
into a Pellet 3D Printer
Implementation Plan — Platform, Wiring & Software
KR 150 / 180
KR C2 Controller
Pellet Extrusion (LFAM)
June 2026

## Slide 2
THE GOAL
A robotic large-format pellet printer
A 6-axis KUKA arm carries a pellet extruder and prints large parts directly from plastic granules — no filament. The heavy-payload arm, the extruder, and the full feedstock chain are in hand; the work ahead is integration, a build platform, and safety.
Pellets in. Big parts out.
150–180 kg
Robot payload — carries any pellet head with margin
~2700 mm
Reach — defines the build envelope & cell size
3–4 kg/h
Extruder output — moderate LFAM throughput
0–350 °C
Melt range — covers PP, PETG, ABS, PA, PC
2
KUKA · LFAM

## Slide 3
WHAT'S IN HAND
Current assets
Robot + Controller
KUKA KR 150 / 180
KR C2 (MP9), KCP2 pendant
480V 3-phase
HAVE
Pellet Extruder
4 kg/h vertical servo
1200 W · 0–350 °C
1.5–3 mm nozzle
HAVE
Hopper Dryer
INTSUPERMAI 110 lb
Dries hygroscopic resins
(ABS, PC, PA, PET)
HAVE
Vacuum Autoloader
INTBUYING XC-300G
300 kg/h · 7.5 L
Feeds the extruder hopper
HAVE
3
KUKA · LFAM

## Slide 4
WHERE YOU STAND
The four subsystems
A
Motion
Robot arm + KR C2 controller
HAVE
B
Extrusion
Pellet extruder, heat zones, nozzle
HAVE
C
Control
Slicer → robot toolpath + extruder sync
TO BUILD
D
Platform
Dryer + feed (done); bed, table, enclosure
PARTIAL
4
KUKA · LFAM

## Slide 5
SYSTEM ARCHITECTURE
What connects to what
CAD Model
STL part to print
Slicer PC
Cura + CuraToKRC2 plugin
→ .src / .dat files
KR C2 Controller
Runs KRL motion program
DeviceNet I/O
BK5120 island
Extruder Control Box
$OUT → RUN/STOP
$ANOUT[1] → speed (0–10V)
$IN ← ready / fault
Robot Arm
carries the head
follows the toolpath
Heated Build Bed
part adheres here
Dryer
dries pellets
Autoloader
vacuum-feeds hopper
SELF-REGULATING LOOPS
Barrel heat · bed PID · chamber · dryer — run on their own, not by the robot.
Amber = robot-controlled in sync with motion Steel = mechanical / feed path

## Slide 6
THE CORE IDEA
The robot does only three things to the extruder
RUN / STOP
Digital output $OUT[n]
Extrude on print moves, stop on travel moves.
SET SPEED
Analog output $ANOUT[1]
0–10 V proportional to sliced flow rate.
READ FAULT
Digital input $IN[n]
Pause the print on an extruder fault.
Everything thermal regulates itself.
Barrel heat zones, the heated bed, the chamber, and the dryer each run on their own controllers. The robot never manages temperature — which keeps the integration small and robust.
6
KUKA · LFAM

## Slide 7
PLATFORM · 1 OF 3
Rigid print table, tied to the robot's base frame
1
Size the build area to the reach — keep it ~1.0–1.5 m square, set 0.7–1.5 m in front of the base.
2
Build a stiff steel weldment with a thick flat top plate (≥15–20 mm) — it must not flex when the heavy arm decelerates.
3
Anchor it to the floor, ideally the same slab as the robot, so they can't move relative to each other.
4
Add 3 hard reference features (dowels / machined pockets) at known XY — these become the base-calibration points.
5
Mount the heated bed on top, on a thermal break so the frame doesn't sink the heat.
BASE FRAME ON THE TABLE
X
Z
Origin + 2 points teach the print coordinate system. Slice Z=0 then equals the real table top.
7
KUKA · LFAM

## Slide 8
PLATFORM · 2 OF 3
Heated build bed — adhesion & warp control
1
Build surface: flat aluminum tooling plate or borosilicate glass, sized to the build area.
2
Heat with a high-wattage 240V silicone pad bonded underneath (LFAM beds run ~1.5 kW to 5 kW+).
3
Control as an independent loop — thermocouple → PID controller → SSR → heater.
4
Mount on the table over insulation + thermal-break standoffs to protect it and save energy.
5
Adhesion: PEI sheet or glue, plus a wide brim/raft in the slice for big beads.
INDEPENDENT CONTROL LOOP
Thermocouple
PID Controller
Solid-State Relay
Silicone Heater
Runs by itself — the robot never sets bed temperature.
8
KUKA · LFAM

## Slide 9
PLATFORM · 3 OF 3
Enclosure, fencing & safety interlocks
Machine guarding (required)
Fence beyond the swept volume, one interlocked door, E-stops inside and out. A KR 150/180 at speed is lethal.
Thermal & fume chamber
Insulated/poly panels keep a warm chamber (~60 °C, up to 150 °C) and contain fumes — duct an extractor out.
WIRED INTO THE KR C2 SAFETY CIRCUIT (X11 / ESC — dual channel)
Door interlock → Operator Safety C8–C10 / C9–C11
External E-stops → C14–C15 / C16–D1
Replace bridges with devices — never leave jumpered
Safety-circuit wiring must be done and validated by a qualified machine-safety integrator — not improvised with permanent jumpers.
9
KUKA · LFAM

## Slide 10
ELECTRICAL & I/O
The DeviceNet I/O island
KR C2
DeviceNet master
BK5120
DeviceNet coupler
MACID 11
KL4004 — Analog Out
$ANOUT[1] → extruder speed (0–10 V)
KL2xxx — Digital Out
$OUT[n] → extruder RUN / heater enable
KL1xxx — Digital In
$IN[n] ← extruder ready / fault
MAPPED IN iosys.ini
ANOUT1=11,0,16,3
outb0=11,8,x3
Full-scale 0x6C00 = 27648 → 10 V
Calibrate so $ANOUT[1]=1.0 → 10 V = max extrude rate. Bench-test before any print.
Power (licensed electrician): 480V 3-phase to the KR C2 sized to its nameplate (~7.5–13 kVA, not the sum of drive ratings). Bed, extruder box, dryer & loader on their own circuits.

## Slide 11
SOFTWARE
From model to robot motion
1
CAD → Cura
Slice the STL in Ultimaker Cura with the CuraToKRC2 plugin.
2
Configure
krl_config.json: tool A/B/C, HOME, Tool & Base numbers, flow constant. Enable Relative Extrusion.
3
Export KRL
Generates native .src / .dat, auto-split into subroutines to fit KR C2 RAM.
4
Transfer
Copy files to the controller via USB or network share.
5
Run
Robot follows the path; writes $ANOUT[1] for flow, toggles $OUT[n] for extrude on/off.
Upgrade paths: KUKA|prc (Rhino/Grasshopper) for simulation & non-planar toolpaths · RoboDK + KUKA.RSI for live streaming (~4–12 ms) — add later, no drive changes.
11
KUKA · LFAM

## Slide 12
CALIBRATION
Tie the model, the nozzle, and the table together
Tool (TCP) — XYZ 4-point
Setup ▸ Measure ▸ Tool ▸ XYZ 4-point
Touch the nozzle tip to one fixed point from 4 orientations; the controller computes the TCP. Enter the tool A/B/C to match krl_config.json. Save as the Tool number.
Base — 3-point
Setup ▸ Measure ▸ Base ▸ 3-point
With the taught TCP, touch the table's 3 reference features: origin, a point on +X, a point in the XY plane. This builds the print coordinate frame. Save as the Base number.
Verify: jog to Base 0,0,0 — the nozzle should sit at the table origin; +X and +Y run along the table edges. Re-touch after any crash.
12
KUKA · LFAM

## Slide 13
ROADMAP
Commissioning sequence
Chart: Indicative effort (days)
| 1 Robot alone (motion check) | 2 Safety circuit validated | 3 I/O bench test | 4 Tool & base calibration | 5 Dry run in air | 6 Heat soak | 7 First print (PP/PETG) | 8 Scale up + engineering resins
Days | 2 | 4 | 3 | 2 | 2 | 1 | 3 | 6
Gate everything on Step 2
Do not run the arm near the table until the door interlock and every E-stop are proven to stop it.
First real print: a single-wall cylinder in PP or PETG (no drying needed) to dial in temp, bead width & flow.
13
KUKA · LFAM

## Slide 14
BUDGET
Remaining spend — entry path
Chart: 
| Safety fencing | Electrical install | Heated bed | Print table | Flange adapter | I/O island | Slicer software
USD | 4000 | 3500 | 2500 | 1500 | 1000 | 300 | 0
~$12.8k
estimated remaining for a working entry-level cell
Already owned
Robot, extruder, dryer & autoloader. Skipping the EtherCAT/drive swap avoids several thousand more.
14
KUKA · LFAM

## Slide 15
WHO DOES WHAT
Three owners, one cell
Licensed Electrician
480V feeder, disconnect, grounding, and the high-power bed/chamber circuits.
Safety Integrator
X11 / ESC wiring of fence interlock + E-stops, and validation that they stop the robot.
You
Table, bed, enclosure shell, I/O island, slicer setup, and calibration — stage and bench-test.
Resolve first: confirm the extruder control box accepts an external RUN/STOP + speed signal. That single answer decides how good the prints can be — check its wiring manual before ordering the I/O island.